Artec Design OÜ, Türi 10c Tallinn, / 11313 Estonia European Union Tel: (+372) 6718 550 / Fax: (+372) 6718 555 / www.artecgroup.com / info@artecgroup.com	Programmable LPC Dongle / DATA SHEET / FPGA based hardware debugger platform

# Features:
- Supports LPC memory read and IO write for POST Code capture
- 4 segment LED display for debug purposes
- 10 bit GPIO header for debug purposes
- Selectable voltage source either USB or LPC bus
- 4 jumper selectable boot images for LPC
- Third party free USB drivers for
  - Windows (98,2000,ME,XP)
  - Linux 2.40 and greater
Included:
- LPC Dongle
- Python based software with source (Linux and Windows supported)
- USB cable
- LPC cable

# LPC dongle interfaces

## LPC
LPC header provides 7 IO pins used for LPC signal (see Dongle schematic). By default 1MB on flash can be accessed over LPC bus (highest MB of 4 MB available in each mode configuration). This can be changed by IO command to full 4 MB.
LPC IO write to address 0x0088 data 0xF4	turn on 4MB addressing
LPC IO write to address 0x0088 data 0xF1	turn off 4MB addressing
LPC IO write to address 0x0080 will be displayed on Post code byte

## Mode Select
Mode select jumpers are intended for internal image selection from dongle flash divided into 4 separate sections.

## GPIO header
GPIO pins are platform pins that are not used in the standard LPC version of the dongle but are target for tailored development for specific functions.

## VCC source select
Jumper is used to define VCC source. When USB cable is used at the same time with connected target board on LPC JMP4 should be off.
## USB
USB interface is used to program dongle flash or read back flash content. This can be done by Artec USB Dongle programming utility.
Usage:
dongle.py -c comport [-vq] filename address
dongle.py [-vqr] offset length filename
Options:
-c	COM port	defines USB to serial comport
-v	Verbose	more messages about operation
-q	Query	Test connection to flash
-r	Readback	Read back flash content
Examples:
dongle.py -c COM3 loader.bin 0
dongle.py -c /dev/ttyS3 content.bin 256K
dongle.py -c COM3 device 1M
dongle.py -c COM3 -r 0x0000 256 flashcontent.bin

USB programming utility can address all of the 4 MB available in any mode that is selected. It must be remembered that only 3072KB to 4090 KB in each mode configuration is directly accessible over LPC without using the 0xF4 command first (see LPC paragraph).